## Slide 1: Assurance – A Practitioners Guide

## Slide 2: Contents
Introduction & Definitions
Organisation & Roles
Assurance Programme
Assurance Framework
Workplace Monitoring
Assurance Activities
Assurance Execution
Acting on Findings
What to Check
Programme Review
Summary

## Slide 3: Introduction

## Slide 4: Introduction
Senior Leadership involvement
Sharing good practice
Publication of process safety performance information
Robust and regular auditing
Constant active engagement and vigilance
Effective Process
Safety Management
Notes: Assurance is a key element of effective process safety management
It allows us to monitor performance, share good practice and engage the whole organisation with the support and involvement of senior leadership
While a key activity is auditing, an effective assurance program is made up of many elements, including periodic activities such as audits along with ongoing monitoring and activities
It should be a process of constant vigilance - Don’t wait for the auditors, maintain a chronic sense of unease

## Slide 5: Defining Assurance
                Assurance - the overarching risk based approach to determine the suitability and effectiveness of our processes
                A programme that captures
                audit
                monitor
                verification and
                review

## Slide 6: What is Workplace Monitoring?
Structured approach to determine effectiveness of control measures
    focus on high risk activities
Monitoring normally conducted by asset leadership team
Confirm work has been effectively planned and being conducted per the plan
    Allows for good practices to be identified and
    leadership presence at the worksite
Trending can provide early indication of potential issues via the identification of weak signals

## Slide 7: Weak Signals
Mind-set shift to welcome these as opportunities to address issues before they become more serious and share the learning
A chronic unease, the feeling when something does not seem / feel right
Using a ‘fresh set of eyes’ it is possible to identify weak signals that may have become normalised by those who work on the asset on a routine basis
These can identify less obvious underlying causes, that can manifest into a more serious issue, e.g.
an unusual noise/ smell coming from an area of the process plant
Gauges / meters giving unexpected readings
inaccuracies in the manner that documentation is completed

## Slide 8: Organisation and Roles

## Slide 9: Assurance Purpose and support
Focal Point
‘Owner’ of the process
Authority, influence, determination and drive, including follow-up activity ensuring timely delivery of sustainable actions
Sponsor
Lead champion with influence and access to the highest management levels
For Example, Operations Director, or similar level
Supports protection of people, the environment, assets and reputation
Assurance
Management drive
Provides confidence & confirmation that risk control measures are working effectively
A key safeguard and to improve performance
Cultural acceptance at every level and buy-in at every tier: CEO to technician
An essential component of management system
Notes: Assurance requires buy-in throughout the organisation.
If done properly is underpins everything we do to protect people environment asset and reputation.
It allows us to confirm that the measures we have put in place to protect us from risks are effective and to drive improvements
It is an essential part of the management system
However it will only be successful with
proactive sponsorship by management,
buy-in from the organisation and
clear ownership of the process and resources dedicated to delivering the program

## Slide 10: Key Roles and Responsibilities
Risk & Assurance Lead (Assurance Focal Point)
Board Members (discharged to the CEO/ MD)
Asset Manager
Technical Director
OIM / Site Manager
Lead Auditor
Technical Authority / Subject Matter Expert
Operations Manager
HSE Director / Manager
Assurance Process Owner
Operations Director
Notes: Assurance affects and requires engagement from the whole organisation
From board members through to senior management
And From corporate HQ through regional, asset and workplace management
It requires a clear focal point to own and drive the program, with active management support
Delivery of assurance activities may engage many people throughout the organisation.
From specialist auditors, through to technical authorities or site managers, who may be asked to lead or participate in assurance activities.
And of course the whole organisation may be asked to engage with the audit process

## Slide 11: Assurance programme

## Slide 12: Plan
That systems and processes for managing Major Accident Hazards are fit for purpose
e.g. Technical audits
That we fully comply with all regulations
and seek out industry
good practices
That we are doing what our systems require
i.e. ‘conformance is compliance’
The rigour and effectiveness of our Management Systems
What might we check?
Notes: It is important to develop a clear plan for assurance activities.
The starting point is to decide what we want our assurance program to check.
This shows a range of things we might want our assurance activity to check, this in turn will derive the type of assurance activities we include in the plan

## Slide 13: Plan the programme
Risk based
assurance frequency
PSM KPI’s
Audit findings
HSE / IVB findings
Legislation change / industry alert
Incident investigation (including near miss)
Engineering judgement
(on/ offshore)
High risk = more frequent
Low risk = less frequent
Factors to consider when setting the scope and frequency of the programme
Notes: Obviously we can’t monitor everything. So how do we decide where to focus our effort?
As part of our operations, we capture a wide range of data and information. Making this available at the planning phase can allow us to develop an initial picture of where our risk areas lie and allow us to use this in developing our assurance program – what we look at and how often
In addition to looking at what the “what is” data is telling us about the status of our controls and barriers, it is frequently useful to consider the “what if” scenarios – how much would our controls and barriers need to degrade to give us a serious problem.

## Slide 14: Assurance programme: rolling
  Frequency must
  support perceived risk
  Frequency must be
  achievable and agreed
  by audit owner
  Confirm frequency enables
  state of process safety barrier to be understood over time
  Scope to address identified risk /
  areas of concern
  Matrix approach of
  assurance
  Confirm scope enables state of process safety barrier health to be understood
  Rolling programme
  with set review points
  Plan reflects all assurance activity
  Supported and agreed by
  Senior Management
  Clear communication plan to ensure all stakeholders are aware
  Assurance Working Group
  Consider both internal and
  external factors
  Process Safety focused
Identify perceived
risk
Develop
audit
scope
Issue / update
assurance
plan
Agree
frequency
Notes: Effective assurance isn’t a one time activity. We need to develop and embed an ongoing assurance cycle as part of our wider management systems.
The process starts with the initial identification of the risk picture using available information and data.
The assurance program and audit scope can be developed based on this. This needs to consider the use of the wide range of assurance tools available and the multiple levels at which assurance activities can be performed.
A key element in MAH risk management is to ensure the program addresses the key process safety barriers.
The priority and frequency of each activity needs to be set to address the perceived risk, but also taking into account what is reasonably achievable. This needs to consider the range of activities, so worksite checks may be on a daily or weekly frequency, while formal audits may be once every year or every few years.
The issued plan needs to be agreed by the key stakeholders and supported by senior management.
As the activities in the plan are completed, this will generate new information, which can be used to update the risk picture and modify the assurance scope moving forward

## Slide 15: Planning
What do we want to learn and / or confirm?
Fully conforming with processes and procedures
Right barriers in place to prevent and mitigate the risk and impact
Confident that systems and processes are both reliable and effective
In-place arrangements meet all relevant regulatory requirements
Fully understand and are prepared for what can go wrong
i.e. risks and consequences
Data and trends from
Safety observation card
Root cause analysis
incident investigations
Subject matter expert judgement
KPIs
MAH barrier models
Previous audit findings
Risk registers content
Legislation changes/Industry alerts
Regulatory findings and advice
Notes: The detailed planning for a specific area needs to take into account some key factors and make use of all the detailed information and data available in this area.
We need to be clear about exactly what each assurance activity, at each level is trying to find out or confirm
We need to identify the relevant information and data which will allow us to understand this and help us develop appropriate checks or question sets to use in monitoring or audit activities

## Slide 16: Assurance framework

## Slide 17: Assurance framework
Each level delivers a different opportunity to understand and improve systems and processes
A ‘blended’ approach gives a better perspective on safety and operational
Select the best people available for the assurance activity being undertaken
Notes: Do we understand what can go wrong: the perceived risk picture?
Do we know what we have to prevent this happening?
Do we know what is required?
Are we confident that our arrangements will work when required?
Do arrangements meet all relevant regulatory requirements?
Success of such an audit requires detailed planning, preparation and engagement and a structured process for execution and closeout

## Slide 18: Corporate and regional audit
Do we understand what can go
wrong: the perceived risk picture?
Do we know what we have to
prevent this happening?
Do we know what is
required?
Are we confident that our arrangements will work when required?
Do arrangements meet all relevant regulatory requirements?
Success of such an audit requires detailed planning, preparation and engagement and a structured process for execution and closeout
Notes: These will be conducted by trained / professional auditors

## Slide 19: Asset level compliance monitoring
Asset level programming
Determined centrally (Assurance Programme Manager) to the risk-based audit schedule
Type of asset level audit
Compliance: specific, pre-set
and open-ended questions
aiding investigation,
enquiry & discovery
Based in the action tracking system for progress monitoring
Audit team
Will be asset supervision with scripted audit question sets.
Notes: Programming
  asset/ site manager should be involved to reflect their perceived risk and knowledge of the asset
  scheduled out 12 months to provide a cohesive coverage
Team
  Aware to capture weak signal / low level observations & to identify trends across all assets and enhance scrutiny
  Auditors should be assigned on a weekly basis by the site manager

## Slide 20: Workplace Monitoring

## Slide 21: Workplace monitoring
Asset / Site Managers responsible for delivery of workplace monitoring programme
Activities planned to align with work activities and to enable periodic updates on significant findings, trends or other matters of concern
Programme takes into account process safety, occupational health & safety and environmental management systems
Typically uses topic specific scripted question sets
Workplace monitoring & behavioural safety are similar in questioning and listening skills
Behavioural Safety | Built around unplanned opportunities
Workplace Monitoring | Built around planned interventions

## Slide 22: Workplace monitoring
Vessel
Operations
Lifting
&
hoisting
Overriding
safeguarding
systems
Risk
assessment
Isolation management
Permit to
work
Control of
work at height
Control of
high energy
hot work
Toolbox
talks
Focus SEMS effectiveness in relation to control measures being impacted via specific task
Notes: SEMS – safety environmental management systems
List is not exhaustive

## Slide 23: Workplace monitoring
Good practice, assessing physical barriers and determine condition by observing an activity by assessment of layout and emergency controls, e.g.
Control system overrides
Relief valves and rupture discs
Locked and normally closed/open valves
Closed / Open drains
Pressure vessels
Electrical control
Small bore fittings (<2”)
Chemical storage and usage
Findings can detect weak signals, e.g.
Compliance with procedures
Life saving rule mitigations
Use of barriers for lifting activities
These weak signals will feed into corporate & regional audits to highlight lessons to be learned

## Slide 24: Assurance Activities

## Slide 25: Assurance activities: System audits
1 | System audits
2 | Technical audits
3 | Compliance audits
4 | Regulatory audits
5 | Workplace monitoring
Focused on management systems (SEMS)
Determines the fitness for purpose of management system
Confirms the system meets industry standards and provides the required level of risk control.
Verifies processes are documented and implemented in line with requirements
Identifies non-conformances and improves the operation of the system being audited
Notes: Add in own case studies if pertinent

## Slide 26: Assurance activities: Technical audits
1 | System audits
2 | Technical audits
3 | Compliance audits
4 | Regulatory audits
5 | Workplace monitoring
Determines fitness for purpose of a specific technical system, such as processes, plant design and operations
Assesses the risk controls and confirms they are proportionate to the risk and ALARP
Notes: Add in own case studies if pertinent

## Slide 27: Assurance activities: Compliance audits
1 | System audits
2 | Technical audits
3 | Compliance audits
4 | Regulatory audits
5 | Workplace monitoring
Confirms organisation actually does what it says
Confirms existing SEMS arrangements are effectively implemented, accounting for human performance
Checks the organisation is meeting the requirements of its own internal procedures and processes
Confirms compliance with relevant statutory requirements and associated guidance documents
Notes: Add in own case studies if pertinent

## Slide 28: Assurance activities: Regulatory audits
1 | System audits
2 | Technical audits
3 | Compliance audits
4 | Regulatory audits
5 | Workplace monitoring
Confirms an organisation’s arrangements to comply with relevant statutory provisions and ALARP risk control
Across SEMS and MAH barrier model, scopes can consider
  hardware components such as Safety and Environmental Critical Element (SECE) barriers
  software such as manning levels, competency/ training and procedures/ operational barriers: the "human" role
  Human machine interface e.g. in areas such as control room operations
Provides important feedback on regulatory compliance but should not be relied upon to find problems
Notes: Add in own case studies if pertinent

## Slide 29: Assurance activities: Monitoring
1 | System audits
2 | Technical audits
3 | Compliance audits
4 | Regulatory audits
5 | Workplace monitoring
Monitors control measures for activities, especially those deemed as high risk
Normally conducted by the asset leadership team
Allows good practices to be identified
Allows trending to identify weak signals and provide insight into underlying causes
Should be viewed as a positive activity, looking for learnings, rather than non-compliances
Notes: Do we understand what can go wrong: the perceived risk picture?
Do we know what we have to prevent this happening?
Do we know what is required?
Are we confident that our arrangements will work when required?
Do arrangements meet all relevant regulatory requirements?
Success of such an audit requires detailed planning, preparation and engagement and a structured process for execution and closeout

## Slide 30: Assurance Execution
Notes: Reminder
Assurance is an overarching approach that captures, monitor (highlight workplace monitoring), verification, review and audit
Includes input from Reports, KPIs, incidents, Risk registers, barrier models etc.
One aspect is to confirm assurance and look for improvement : check, verify and understand what it is we want to understand.
Next sections consider how to performing a review of a site, how to report and manage findings.
Always important to consider Plant / People / Process

## Slide 31: Terms of Reference
Objective
Why is the assurance activity needed and what it looks to achieve
Ideally with a ‘problem’ statement or ‘improvement’ opportunity identified
Fieldwork details
How the assurance activity will be delivered
this can include review of documents, discussions and interviews and site visits
Can include plant, people and process
Scope
Identifies the activities to be included and what isn’t going to be included
Use the phrase ‘and will not be limited to’ to allow for any organic growth
Notes: ToR Terms of Reference – route map to delivery of assurance with site, people and fieldwork.
Scope –
To identify issues from strong and weak signal, MAH and compliance focus.
Clearly states the boundaries of the activity and important to keep focus on outcomes
Answers the questions
- what can go wrong and what are the practices in place to protect?
- Does the auditee know what's expected?
Remote considerations : Fieldwork
Consider practicalities of how it will be conducted.
It will take more planning and preparation effort.
e.g. Gettings documentation early, knowing the people / roles and timings that may be needed and how to witness activity (if possible)
Page 22 of Guidance

## Slide 32: Kick-off meeting
Opportunity to engage with the auditees
Output is to issue the draft ToR for review and comment
Awareness of ‘weak signals’ should be emphasised
What are the ‘niggles’, or recurring issues
Can identify ‘real time’ opportunities to observe site activities furthering personnel engagement
e.g. a complex lifting operation, a confined space entry activity or a break of containment
Notes: ToR – Terms of reference
Talk from different assurance activity perspectives.
Kick–off – get the early engagement, opportunity to get early feedback on ToR.
Important to listen, especially if weak signals or niggles are shared and might needed more exploration.
Identify where real time witnessing of activities can occur.
Remote : discussing here any potential issues including logistics of witnessing activity.
Pages 23-24 of guidance

## Slide 33: Fieldwork: planning and preparation
Sample sizes are statistically based or through professional judgement
  Accounting for available resources and time
  The lower the acceptable risk the greater the sample size
Office-based preparation essential to maximise time validating on site
Preparing question sets ensures thoroughness, consistency and efficiency
  Question set can be shared to assists auditee preparation
Notes: Important to restate that 100% review are not effective, sampling is a sensible alternative scaled to the needs at the time.
Samples should be selected by the team, try not to be guided by the auditee.
Question sets useful to ensure nothing is forgotten, but also to share if being conducted multi-site for consistency.
When preparing consider soft barriers, including resource levels, competency etc.
The thorough planning here will aid remote assurance.
Pages 23-24 from Guidance (includes reference to National Audit Office – Practical Guide to Sampling)

## Slide 34: Fieldwork: team preparation
Audit Team
Auditors understand good audit practice and team have confidence to ask questions
Clear roles assigned
Ideally team should consist of a lead auditor and one team member, and
  Will be independent of the business area being audited
  Reduces chance of bias from one auditor’s preference
  Allows for a blend of skills and experience
  Helps with discussions, one auditor asks a question the second records and provides additional perspective
Notes: Blend the skills and experience of the team for a better outcome.
Team is better than solo, one lead and (at least) on other, both who are familiar with the audit process.
Team members able to ask pertinent questions.
As an audit team, essential to keep engaged with the auditees.
Page 24 in Guidance.

## Slide 35: Fieldwork: opening
On-site fieldwork, start with short opening meeting to
  Introduce the audit team
  Clarify the scope, make adjustments to scheduled activities and schedule close out meeting
  Provide the opportunity for an auditee presentation
  e.g. overview of the business area and objectives, key activities and any particular health and safety concerns
  Agree audit team escorts
  Discuss post-audit requirements e.g. reporting, corrective actions and follow-up
Notes: Your prior communication and engagement will make this opening meeting go smoothly
The opening meeting is a 2 way progress, sharing what will be done, but also an opportunity for the auditee to give an overview of the area to be audited.
Agree timings, determine any activities to be actioned.
Highlight how this will proceed day by day and the expected outcomes.
Remote meetings – listen, give plenty opportunity for discussion and feedback
Pages 24 and 25 of Guidance

## Slide 36: Fieldwork: engaging
The audit team will engage on site and obtain evidence of compliance, identification of issues, improvement opportunities and
good practice
Meet auditee representatives at the close of each day to
  provide feedback
  potential non-conformances, and
  provide clarification
Notes: Good practice is to do this daily but remote auditing may require a different approach for practical reasons.
Key aspects are to -
- Listen
- Witness
- Check and Verify
- Eyes open
- Situational awareness (out on site)
Feedback at end if each session, summarise each day. Highlight positives as well as any negatives to provide balance.
When engaging in the fieldwork, be mindful of the human barriers – are they effective or at risk of error. Are procedures clear or unwieldy?
Page 25 in Guidance

## Slide 37: Fieldwork: feedback
At the end of the fieldwork, conduct short feedback session:
  Allows confirmation and agreement on findings
  Opportunity to provide feedback
  Ensures no surprises in draft report
  Feedback includes strengths and good
  practices and detail the next steps
Notes: Highlight positives and negatives.
With regular updates have been given during the process there should be no surprises.
Get agreement on any findings and receive any feedback in a positive manner.
Additional follow up may be required due to remote efforts
Page 25 in Guidance

## Slide 38: Fieldwork: closing
If required report will be succinct and factual
  Have a clear summary covering the findings or concerns and highlights good practice
  Escalate any findings of note as required to promote learning
Closing meeting allows agreement of draft report and agree finding prioritisation
  Feedback from this meeting should be incorporated into the final audit report
Notes: Draft report in 7 days after closing meeting
Report to be succinct, not a full download. A good summary highlight both good, findings and actions.
Page 26 in Guidance

## Slide 39: Recording and review
It is important that findings and remedial actions from the assurance programme are understood & accepted
Define & agree the prioritisation criteria to address remedial actions
Follow-up to confirm that:
Assign clear accountabilities and responsibilities for who will complete the remedial actions
Always be open to updating or changing the assurance programme based on latest evidence & information
Actions have been implemented & closed to the required standard (with supporting evidence)
Ensure that your workforce have the necessary capability to carry-out their assigned actions
Agree suitable response timescales (based on risk level)
i.e. training & competence and capacity (time & resources)
Following suitable review, that the action has resulted in an effective & sustainable 'fix’
Notes: What - are they addressing
When – Priority
Who- Capacity and resource, do they have time to address the actions
Ensure there is clarity on the actions and how they address the findings
Page 26 in Guidance

## Slide 40: Findings
Some findings will be significant (or occur frequently) and should be reported to board
Actions will be recorded and tracked in the business action management
system
  Prioritisation of actions will be commensurate with associated risk
  Actions should be SMART & sustainable
  Corrective actions address the root cause
  Avoid generating too many actions
  A lack of audit actions should be challenged
Notes:   SMART (specific, measurable, achievable, realistic, time bound)
  Some findings may need to be escalated, possibly to board level
  Human barriers are weak and errors can be made. Where possible try to improve procedures , processes etc.
  Too many actions can dilute their benefit, 4 good actions can be better than (say) 20 general actions
  Page 26 in Guidance

## Slide 41: Acting upon findings

## Slide 42: Acting on findings
  Acting upon findings can be difficult due to:
  Different perceptions of those being audited
  Too many findings
  Unclear prioritisation
  Unclear or un-specified recommendations and open ended actions
  Findings allow opportunities to improve, with actions to close gaps and improve performance
  Leadership to be aware of significant gaps and
  to support their resolution
Notes: See findings from both sides, auditor & auditee
Help focus actions to address the key findings
- can be useful to adopt the "less is more" approach
> SMART <
Page 33 in Guidance

## Slide 43: Improving through findings
  Underlying causes
  Can be added to the wider audit programme to ensure not replicated in other areas
  Allows less significant findings to be identified to address with increased priority / resources
  There can be resistance to findings around weak signals as they require greater scrutiny
  Repeat findings can be escalated as the previous actions have been unsuccessful
  Important to bring findings together and provide a cumulative view of findings
Notes: Have data, information to support findings and be prepared to follow up in more detail if needed (especially around weak signals)
Page 33 in Guidance

## Slide 44: What to check
Notes: Process overview – Health check.

## Slide 45: What to check: process
  How well are our assurance processes working?
  Are the completed audit activities providing good quality
  output?
    Are we identifying true weaknesses?
  Are identified issues analysed to identify root cause?
  Is there sufficient coverage across the four different types of audit?
  Does the plan cover the robust verification of activities in relation to people, plant and process?
Key statements to be considered:
Notes:     Are audits identifying true weaknesses? or has the exercise become a tick-box exercise?
  Reminder of the 4 different types of audit (System, Technical, Compliance, Regulatory)
  Confirm we are using the correct type of audit at the right time
As we progress through schedule keep an eye on the health of the program
An ongoing check and balance on what we set out to achieve vs what has been achieved.
Ensure value is gained from the activity
Page 32 in Guidance

## Slide 46: What to check: improving
Are we sharing good practice?
What is the status of barriers against MAH, and which areas of our SEMS need further focus?
  Reporting to the various levels of management
  Senior management summary reports with schedule and action status, key risks, and any trends / KPIs
Are we making improvements?
What information is available to steer future monitoring and audit plans?
  Additional audit / monitoring focus based on Regulatory findings and incident statistics
  Significant activities / changes planned affecting the SEMS?
    Opportunity to audit activities / changes in advance to prevent an issue
  Are there weak signals requiring action or follow up to align with other sources, e.g. investigations
Notes: MAH – Major Accident Hazard
SEMS – Safety Environmental Management System
KPI – Key Performance Indicator
Ensure a clear view of barriers, sharing what is found and making improvements.
Any changes that could mean adjusting the schedule or scopes based on feedback and /or weak signals.
Page 32 in Guidance

## Slide 47: Programme review

## Slide 48: Engagement
Lessons learned slides can be shared with specific audiences on mind
Upon completion, audit team reviews what went well and what could be improved through the audit process
With a range of locations & auditors it is worth review and reflection to determine if outcomes are site specific or a broader systemic issue
Notes: Keep engagement throughout.
Keep in touch with the site as resolution of findings progress, being mindful of other sites / locations for Lessons Learned.
Page 27 in Guidance

## Slide 49: Programme review
It is important to review assurance programme annually (with a team) to determine if it is fit for purpose and delivering on expectations.
They would look at:
Programme structure and if it addresses key MAH threats across all business areas?
Is programme being driven by a suitable ranking of risks?
Does programme look at system, technical, compliance and regulatory audits?
Audit team composition – being spread across the business to incorporate subject matter experts?
Are audits being completed on time?
Are report findings being read and discussed through the organisation?
Are audit report actions being completed on time?
Are there any underlying causes?
Performance against Key Performance Indicators
Notes: We mentioned before that assurance needs to be an embedded process – part of the management cycle.
A key part of this is to continue to review how effective the assurance program itself is.
Are we looking at the right things?
Are we involving the right people?
Are we actually completing the program as planned?
What are we finding?
What are we doing about the findings?

## Slide 50: Summary

## Slide 51: Overview
Assurance – a key aspect of a healthy SEMS. It will reduce the risk of major accident, provide confidence risk control systems are effective, identify weak signals, engages positively with the workforce and contributes to barrier strength
Publication of process safety performance provides important assurance about the management of risks by an organisation
Sharing good practice across industry sectors to learn and implement lessons
Assurance review committee to look at trends and sustainability of actions
A culture of welcoming ‘bad news’ that allow for improvements
1
2
3
4
5
6
Effective Process
Safety Management
Robust and regular auditing of SEMS and associated MAH barriers, ensures weaknesses are identified and process safety risks are effectively managed
Notes: This presentation has covered a lot of material, so let’s remind ourselves that fundamentally what it is all for is to make sure we continue to effectively manage process safety
Assurance is about
Building confidence in our controls
Using weak signals to identify issues early
Building engagement through all parts of the organisation
Assurance provides a framework to:
Share performance, lessons and good practice
Correct issues and drive improvement
But it doesn’t come for free, and it is not just something that is done to us.
We should not treat it as a threat, a culture which welcomes “bad news” or weak signals as an opportunity to correct an issue early is in the long term going to be more successful than one which waits for the problem to occur
It is above all a collaborative effort across an organisation to protect its people, our environment and the business

## Slide 52: Summary
An effective assurance plan or programme will help to protect your people, assets, environment, reputation and business performance. KPIs will provide visibility to leadership.
Good preparation and planning is critical to the success of your assurance programme. A ‘blended’ approach will shape the risk-basis (including weak signals), inform various levels and scope of the programme and ensure the allocation of necessary resource to deliver it.
Prioritise the assurance plan or programme in your messages to the business, appoint a dedicated Leadership Sponsor or ‘Champion’, provide the necessary resources & space to ensure full engagement by the workforce and, most importantly…..take part!
Agree and establish criteria for how the outputs from the assurance plan or programme (i.e. identified gaps and ‘weak-signals’) will be systematically captured, analysed and acted upon. Actions are based quality not quantity.
Strategy
Plan
Enable
Recording and review

## Slide 53: https://oguk.org.uk/product/assurance-toolkit/